## Slide 1: License Plate Recognition From Still Images and Video Sequences: A Survey
Based on Anagnostopoulous Paper
Presented by: Krikor Hovasapian
ECG 795 4/25/2013

## Slide 2: Agenda
Introduction
License Plate Detection
Character Segmentation
Character Recognition
Conclusion
Notes: Where available, we will discuss performance, execution time and the platform used.

## Slide 3: Introduction
License Plate Recognition (LPR) is a core module used in various applications. (i.e. toll payment, freeway and arterial management for traffic surveillance)
Three Steps
  License Plate Location
  Plate Character Segmentation
  Determining/Recognizing Characters
Requirements
  Should be quasi or near-real time (~50 ms)
  May be application dependent

## Slide 4: License Plate Detection
3 categorization methods are proposed:
  Binary Image Processing
  Gray Level Processing
  Color Processing

## Slide 5: Binary Image Processing
Combination of edge statistics and morphology.
Process used:
  Compute Gradient Magnitude and Local Variance
  Look for significant changes in brightness around LP region.
Advantage: Fast/Relatively high LP extraction Rates
Disadvantage(s): Very sensitive to unwanted edges in complex images.
Papers: [1] – [4] in Survey
Notes: Gradient Magnitude computation from class: Discuss
How would get the local variance? (LOOK UP)
How can you reduce the sensitivity for the unwanted edges in complex images? (LOOK UP)

## Slide 6: [1] – Martin, Garcia, and Alba
“Top Hat” algorithm that can detect small objects of different brightness.
Success rate: 80% of license plates detected
Disadvantage: Camera/Vehicle distance dependency.
Similar work: Wu et al [77] gives 93% accuracy
Notes: My understanding: Not sure what the optimal distance would be to discern the region in the image where the License Plate may exist based on this algorithm. What happens when you’re too close to the plate? What happens when you’re too far? According to the paper: highly dependent on the dimensions of the binary object. Obviously there has to be some equilibrium.

## Slide 7: [2] – Hongliang and Changping
Hybrid approach to edge detection and morphology for highway ticketing systems.
Process used:
  Vertical Edge Detection
  Edge Statistical Analysis
  Hierarchical based LP location
  Morphology based LP extraction
Success rate: 99.6% of license plates detected (9786/9825 images)
Disadvantage: Depends heavily on a fixed distance and angle of the camera.
Notes: My understanding: Limited application, and possibly well suited for highway ticketing systems. One thing that wasn’t clear to me in the survey paper is that the results are based on a priori knowledge of the license region. So obviously knowing where the license plates should be will more than likely inflate your results/accuracy.

## Slide 8: Honorable Mention…
CCA (Connected Component Analysis) – Scans a binary image and labels it’s pixels into components based on connectivity (4-connected or 8-connected)
Then… using Spatial Measurements:
  Grab Area, Orientation and Aspect Ratio of the connected components.
  Filter out binary objects that exceed the desired limits.
Notes: Look up notes from class on connected components… Also understanding of 4-connected and 8-connected from earlier in the semester…

## Slide 9: Honorable Mention…
Zheng et al. Vertical edges of car image along with a sobel operation, perform some filtering of background and reduce image noise, to get:
97% Success Rate with total processing time of 47.9 ms on a 384 x 288 px. image.
Image taken from: Anagnostopoulos et al. License Plate Recognition From Still Images and Video Sequences 2008
Notes: Sobel operator…..

## Slide 10: Gray-Level Processing
Seven methods proposed in survey:
  Global Image Processing
  Partial Image Analysis
  Statistical Measurements
  Hierarchical Representation
  Probabilistic Object Tracking in Videos
  Region Segmentation
  Image Transformation
Notes: Global Image Processing – Using contrast variations across the entire image to determine where the LP exists.
Partial Image Analysis – Where the vehicle is scanned with N-row distance, counting the existent edges (like previous slide)
Statistical Measurements – Block-based gray-level processing, where blocks with a high edge magnitude or variance are identified as LP regions when certain geometrical criteria like area and aspect ratio are satisfied.
Hierarchical Representation - Vector quantization, which models the probability density functions by the distribution of prototype vectors. Another way of looking at it is taking a large set of points, which are vectors and placing them into groups that have approximately the same number of points that are relative to them. Examples in the paper use VQ or some striping method across the image to locate the region that has high contrast between the text and background.
Probabilistic Object Tracking in Videos – Find the license plate and track it in successive video frames by following the probability density function propagation using condensation algorithm

## Slide 11: Region Segmentation
Sliding Concentric Windows (SCW) proposed in Anagnostopoulos [39]
Used to find the local irregularities in the image.
Process Used:
  Image statistics such as standard deviation and mean value are used as “heuristics” for locating the License Plate.
  Uses concentric windows X1 x Y1 (inner) and X2 x Y2 (outer) to slide across the image from left to right and top to bottom.
  At each pixel the standard deviation and mean value are calculated.
  Based on some user defined threshold, if the ratio of the two statistics is exceeded, then the pixel is considered to be part of the License Plate.
Success Rate: 96.5% plate localization
No mention of performance metrics in survey.

## Slide 12: Region Segmentation
Image taken from: Anagnostopoulos et al. License Plate Recognition From Still Images and Video Sequences 2008

## Slide 13: Image Transformation
A good number of papers cited use some form of image transformation
[21] used Gabor Filters for texture analysis and reported 98% success rate for LP detection.
Disadvantage: Acquisition on fixed and specific angles with small sample images. Computationally expensive and slow.
[25] used a combination of Hough Transform and Contour Algorithm, which produces higher accuracy/faster computation for RT systems.
Success Rate: 98.8% (average)
Disadvantage: HT is also computationally expensive if used on binary images with greater number of pixels.
Notes: Gabor Filters – Linear filter used for edge detection. Good for texture description and discrimination.

## Slide 14: Image Transformation
Wavelet Transform for extracting important contrast features.
Subimage divided into 4 regions: (LL,LH, HL,HH)
Success Rate: 92.4%
Disadvantage: Unreliable when the distance between the vehicle and camera is too close/far.
Image taken from: Anagnostopoulos et al. License Plate Recognition From Still Images and Video Sequences 2008

## Slide 15: Color Processing
Techniques make use of expected plate appearance in each country.
Unreliable due to how natural scenery can change color when lighting conditions are unstable.
Color specific and country based. No uniform solution, yet.
3 methods:
  Color Model Transformation
  Fuzzy Set Theory
  Histogram Processing
Notes: Plate background and text color.

## Slide 16: Color Model Transformation
[7] and [43] propose that a color combination of plate and character is unique.
Shi et al. propose classifications of Chinese LP’s using HSL (hue, saturation, lightness) color model with 13 categories.
After classification of regions, the AR of the expected plate is then verified.
Notes: Dark blue
Blue
Light Blue
Dark Yellow
Yellow
Light Yellow
Dark black
Black
Gray Black
Gray White
White
Light White
Other

## Slide 17: Fuzzy Sets Theory
Set of rules to help describe and locate LP’s in images.
Use membership functions:
  “bright”
  “dark”
  “bright and dark sequence”
  “texture”
  “yellowness”
Gives horizontal and vertical plate positions.
Notes: Dark blue
Blue
Light Blue
Dark Yellow
Yellow
Light Yellow
Dark black
Black
Gray Black
Gray White
White
Light White
Other

## Slide 18: Example… Zimic et al [18]
Based on rules for human perception.
Brightness and Darkness are defined by interval [0, 255].
Input image is partitioned into 75x25 pixels.
Each partition computes the four properties.
Success Rate: 97%
Disadvantage: Rules 2 and 4 limit distance.
Notes: “Bright Rectangle area within which there are some dark areas”
“Located approximately in the middle or lower middle part of the image”
“The border of the plate is bright”
“The approximate dimension of the plate is 530 x 120 mm.
Input Image = 768 x 576 pixels
Processing time was reduced from 4s to 2s by looking at every fourth line in the image.

## Slide 19: Results
Notes: As expected, the expermination setups are well controlled to obtain predictable scene features, such as perspective, distance, background and illumination.
Typically, IR auxillary units have been used due to the nature of LP’s retroreflective material
Most papers have disclosed that there is always a tradeoff between detection accuracy and minimum plate resolution.
Table 1 shows the minimum plate resolution, where the vertical resolution of the plate is between 10 to 16 pixels. Unfortunately, these dimensions are not sufficient for segmentation and extraction of characters and are only ideal for detecting where the plate exists in the image.
Segmented and proper recognition will require vertical resolution to be between 20-40 pixels, but some papers have shown that given a sufficiently good condition LP, a height of 20-25 pixels will suffice for proper segmentation and recognition of characters.